## Slide 1: KRGSA Groundwater Sustainability Plan (GSP) Final Draft
Kern River Groundwater
Sustainability Agency (KRGSA)
Public Hearing
KRGSA Board Meeting
December 5, 2019

## Slide 2: KRGSA Sustainability Goal
Manage groundwater resources sustainably in the KRGSA Plan Area to:
    support current and future beneficial uses of groundwater including municipal, agricultural, industrial, domestic, public supply, and environmental uses
    optimize conjunctive use of surface water and groundwater
    avoid or eliminate undesirable results over the implementation and planning horizon.
DRAFT
Notes: edited

## Slide 3: KRGSA GSP Organization
1 Administrative Information
2 Plan Area
3 HCM/Groundwater Conditions
4 Water Budgets
5 Sustainable Management Criteria
6 Monitoring Networks
7 Projects and Management Actions
8 Implementation Plan
9 References and Technical Studies
DRAFT

## Slide 4: KRGSA GSP Plan Area
361 square miles
13% of the Kern County Subbasin
Composed of:
  City of Bakersfield
  Improvement District No. 4 (KCWA)
  Kern Delta Water District (KDWD)
  Additional smaller agencies
DRAFT

## Slide 5: Land Use in the KRGSA Plan Area
North – Urban
South – Agricultural
2015 Land Use
  41% - Agricultural
  33% - Urban
  26% - Undeveloped
DRAFT
7th Standard Rd

## Slide 6: Active Wells in the KRGSA
162 Municipal wells
67 Public Supply and Small Water System wells
151 Industrial, Domestic, and other Private wells
642 Agricultural wells
54 Banking recovery wells
DRAFT
7th Standard Rd
Notes: More than 1,000 active wells in the KRGSA

## Slide 7: Preliminary Management Areas (MA)
Based on land use and well use
  Urban MA – 41%
  Agricultural MA – 57%
  Banking – 2%
DRAFT
Urban MA
Agricultural MA
Banking
MA

## Slide 8: Sustainability Indicators
Chronic Lowering of Water Levels
Reduction of Groundwater Storage
Degradation of Water Quality caused by management actions
Land subsidence affecting land use
Depletion of Interconnected Surface Water affecting beneficial use
If a sustainability indicator is determined to be significant and unreasonable , then it is an Undesirable Result
DRAFT

## Slide 9: Balance High and Low WLs
Municipal wells went dry or experienced problems during drought – keep water levels above historic lows
Agricultural and banking wells require lower water levels
Balance needs of KRGSA wells
DRAFT
7th Standard Rd

## Slide 10: Reduction of Groundwater in Storage
3 Independent Methods
Relatively good agreement
Minimal deficits; sustainable budget
Deficit for banking adjustments

## Slide 11: Projected Water Budgets Future Deficits
DRAFT
Increase urban demand
Decrease SWP supply
Increase agricultural demand (climate changes factors )
Potential Future Water Budget Deficits
Plus Historical Adjusted deficit of -29,000 AFY

## Slide 12: Projected Water Budgets C2VSimFG-Kern Model
DRAFT
Baseline - current land use and projected water supply and demand
2030 Climate Change Scenario with increases in agricultural demand and decreased supply
2070 Climate Change Scenario with further increase in demand and decrease in supply
Model simulates the physical system and includes recharge in the KRGSA for and by others;
KRGSA is planning for larger deficits than indicated in the model.

## Slide 13: Constituent of Concern Arsenic
Focus on constituents affected by management actions
Arsenic concentrations increase with declining water levels
More than 25 wells with detections above the MCL
Widespread issue in the Plan Area
DRAFT
7th Standard Rd

## Slide 14: Inelastic Land Subsidence
Historical Subsidence from 1926 – 1970 mapped by USGS
Up to 9 feet in southern Plan Area
Correlates to areas of clay soils and subsurface clay sediments in southeast Plan Area
DRAFT
Clay Soils
Kern Lake Bed
Clay Soils
7th Standard Rd

## Slide 15: Subsidence and Critical Infrastructure
Critical infrastructure includes pipelines, canals, utilities, structures, wells, transportation
No damage to critical infrastructure in the Plan Area identified to date
Set minimum thresholds to mitigate future subsidence
DRAFT

## Slide 16: Analysis of Interconnected Surface Water
DRAFT
Evaluated groundwater conditions using local NCCAG* maps along Kern River
Kern River is actively managed through regulated releases, diversions, and managed aquifer recharge
Kern River
*NCCAG - Natural Communities Commonly
Associated with Groundwater
More than 80% of the flow is diverted above the Calloway Weir
River was dry below the Calloway Weir more than 25 % of the time
Groundwater is deeper than 50’ below the river throughout the entire KRGSA

## Slide 17: Analysis of Interconnected Surface Water
DRAFT
Evaluated groundwater conditions at local NCCAG areas in southern Plan Area
Analysis indicates that local vegetation and wetlands are not supported by groundwater in the Principal Aquifer
*NCCAG - Natural Communities Commonly
Associated with Groundwater
Mapped areas include recharge basins, spills along the rim canal, artificially-constructed ski lakes. Local irrigation and perched water conditions throughout the area.

## Slide 18: Sustainability Considerations
WL below screens in Municipal Wells
Ability of banking recovery wells to recover water
Arsenic in Municipal Wells
Deficits for Projected Water Budgets
Historical subsidence
DRAFT

## Slide 19: Approach to Minimum Thresholds
Undesirable results relate historic low water levels; keep urban wells near historic lows.
Allow operational flexibility for banking wells to recover critical supplies during drought.
Measurable Objectives are selected as the midpoint for an operational range.
Keep MTs and MOs SIMPLE to facilitate management.
DRAFT

## Slide 20: Approach to Undesirable Results
Add number of wells and duration to refine definition of undesirable results.
DRAFT

## Slide 21: Assignment of Minimum Thresholds (MTs) and Measurable Objectives (MOs)
Example hydrograph from monitoring well
In Urban MA, MT is set at the historic low water level
The MO is the average between the high level and the MT
DRAFT

## Slide 22: Improved GSP Monitoring Network
39 wells identified
Improved well selection
Added inactive wells to replace production wells
Water level monitoring only
Best use of other WL programs
Incorporates water quality data from numerous existing programs
DRAFT

## Slide 23: Adjustments to MTs: Input from Small Water Systems
Modified Minimum Thresholds (MTs) at request of Lamont and Fuller Acres
Consistent criteria with Urban MA
Modified MTs in 3 separate areas as requested by 4 separate Small Water Systems
DRAFT

## Slide 24: KRGSA Subsidence Monitoring
Water level monitoring
Three GPS stations for screening
InSAR Subsidence available from DWR (on 1-mile grids)
Coordinate with KGA and other GSAs for regional Subbasin-wide subsidence monitoring
DRAFT
7th Standard Rd
NASA/JPL May 2015 – Dec 2016

## Slide 25: GSP Projects to Address Future Water Budget Deficits Up to about 150,000 AFY of additional KRGSA supply
Project | Description | KRGSA Project Water
Water Allocation Plan | KDWD plans to use its full Kern River entitlement as prioritized in its Water Allocation Plan (WAP) for the Agricultural MA. The WAP total average supply has been corrected for planned sales to NKWSD. | 20,797 AFY
Kern River Optimized Conjunctive Use | The City plans to use its full Kern River entitlement, less current obligations, to mitigate undesirable results for water levels and water quality in the Urban MA. | 89,619 AFY
Expand Recycled Water Use in the KRGSA | The City will increase recycled water use inside of the KRGSA from its WWTP No. 3 in 2026 when a contract for use outside of the KRGSA expires (about 72% is currently used outside of the KRGSA). | 11,556 to 13,407 AFY
Conversion of Agricultural Lands to Urban Use | Approximately 10,000 acres of current KRGSA agricultural lands is expected to be urbanized; this future urban demand is already included in the projected water budget, so 100% of this agricultural water use represents a demand reduction. | 27,000 AFY
ENCSD North Weedpatch Highway Water System Consolidation | Up to six small water systems in the northeast KRGSA will be consolidated into the ENCSD system for benefits to drinking water quality, including to disadvantaged communities (DACs). | No new supply; improved water quality to DACs
Possible Water Exchange | KRGSA member agencies can perform exchanges of surface water and groundwater for benefits to water quality, including to DACs | No new supply; improved water quality to DACs
DRAFT

## Slide 26: Key GSP Projects
DRAFT
  Optimizes Kern River recharge across the southern Plan Area
  Reduces groundwater pumping
  Allows local maintenance of water levels
  SEIR completed 2018 – implementation initiated
KDWD Kern River Water Allocation Plan

## Slide 27: Key GSP Projects
DRAFT
  Prioritizes use of City’s available Kern River water
  Increasing water availability over the implementation and planning horizon
  Allows municipal pumping to be reduced to avoid undesirable results
  Meets future projected water budget deficits for urban demand
City of Bakersfield Optimized Conjunctive Use

## Slide 28: Key GSP Projects
DRAFT
Consolidation of up to six small water systems with ENCSD to address water quality concerns: nitrate, TCP, and arsenic
Grant funding through the DWRSF program
Improves drinking water quality for disadvantaged communities in the KRGSA
East Niles Community Services District
North Weedpatch Highway Consolidation
1,2,3-TCP Wellhead Treatment

## Slide 29: Projected Water Budgets with GSP Projects
DRAFT
GSP projects and address current and projected water budget deficits to achieve sustainable management.

## Slide 30: Management Actions – KRGSA Policies
DRAFT
5-Step Action Plan if Minimum Thresholds are exceeded
Optimize Conjunctive Use in the KRGSA
Implement a Well Metering Program
Implement a groundwater extractions Program
Support CA Delta Conveyance to Preserve Imported Supplies
Incorporate Climate Change Adaptation Strategies
Support Sustainable Groundwater Supplies for KRGSA DACs
Improve Groundwater Monitoring Program
Incorporate a Policy of Adaptive Management in the GSP Process

## Slide 31: Additional Changes/Additions to Draft GSP New Lands Added
DRAFT
Agricultural lands in southwest
Urban/Mixed land uses in southeast
Total 1,847 acres (less than 1% of previous Plan Area)
Eastern lands already in water budget; small water use in southwest (1,300 – 2,500 AFY)
New Appendix K of the GSP
Agricultural Lands in southwest
Residential/ Mixed Use in east

## Slide 32: Public Comments on the Draft GSP
DRAFT
Chevron NA – meeting 2-14-19; email comments 8-5-19; 10-24-19
  Response: All comments discussed and incorporated
Leadership Counsel letter 7-10-19; letter 11-26-19
  Response: Letter from KRGSA 8-13-19
  Response: Reviewed comments; clarifications to GSP, as applicable
California Department of Fish and Wildlife
  Response: Reviewed comments; clarifications to GSP, as applicable
City of Los Angeles
  Response: Revised recycled water amounts on Table 2-1 (revised to 11,321 AFY)
  Response: Modified discharge provided from February through September
  Response: Provide notifications regarding any future GSA actions
Notes: In the presentation, I’ll dismiss Chevron comments (already completed) and the City of LA comments. I worked with Art to get the correct edits in the document, emailed them to him and he is making sure that Ginny and others say ok. Then I’ll proceed with comments from Leadership Counsel and the CDFW.

## Slide 33: Public Comments Leadership Counsel for Justice & Accountability
23-page letter of perceived deficiencies/un-met requirements
Numerous Comments Claim non-engagement of Small Water Systems and DACs
  Response: 1st meeting with Small Water Suppliers July 2017; numerous outreach meetings and 2 Open Houses; ongoing relationships between GSA members and Small Water Systems; GSP projects and management actions target DACS; Adjusted MTs based on Small Systems input; many other activities
  Response: Lamont PUD joined the KRGSA after the Draft GSP was prepared; edits and adjusted MTs based on their input; may add Lamont PUD MW to GSP program
Attached technical analysis on 3 issues (responses on following slides):
  Water Budget Checkbook and Future Water Budget Hydrology
  Water Quality
  Dry Well Analysis
DRAFT
Notes: This is the one slide that I’m still working on. The remaining slides discuss the three bullet items in the technical analysis above.

## Slide 34: Response to Public Comments – Water Budget Leadership Counsel for Justice & Accountability
Comment: Checkbook doesn’t account for subsurface outflows that could impact recharged water
Response: Model analysis does account for subsurface outflows
  Recharge used to maintain water levels; seasonal recovery with local wells (not all water is banked long-term)
  Conditions are dynamic and will change over time
  Water budget components and MTs/MOs monitored
Comment: Projected Water Budget hydrology not variable
Response: Contains both the wettest year and driest year in the 50-year period and period of largest water level fluctuations in most areas
  Compares to rainfall and streamflow over a 50-year period
  Explained in detail in the model documentation (Attachment 1)
DRAFT

## Slide 35: Response to Public Comments – Water Quality Leadership Counsel for Justice & Accountability
Comment: TDS, nitrates and arsenic are actively managed and programs are described adequately (no response required)
Comment: Includes suggestions for Annual Report (noted)
Comment: Pesticides not detected above MCLs (no response required)
Comment: Suggest clarifying language on local management (considered)
Comment: Questions on sources and impacts to wells (response – management actions and monitoring program will address these issues)
Comment: Provide additional information on 1,2,3-TCP (response – noted in GSP that the KRGSA will be analyzing TCP water quality data)
DRAFT

## Slide 36: Public Comments – Dry Well Analysis Leadership Counsel
Provided a “Dry Well Analysis” of the Minimum Thresholds (MTs) and Measurable Objectives (MOs)
Places a 2-mile blue-bubble radius around the monitoring wells
Count number of wells going “dry” for each MO or MT bubble
Out of 3,633 wells, predict six or seven domestic wells will go dry
DRAFT
6 to 7 Domestic Wells
Blue Bubbles are GSP Monitoring Wells
Larger no. of wells include monitoring, remediation, cathodic, test wells, etc.

## Slide 37: Response to Public Comments – Dry Well Analysis Leadership Counsel
All “dry wells” are in Urban MA where higher water levels are maintained
MO is average water level; if 159 wells go dry every time water levels are “average” or below, they have been dry for a long period of time (i.e., 1990s)
MT is historic low level – well would have been dry before any GSP action was taken
Located in City/Cal Water/OMWC service areas; pumping reported to ID4
DRAFT
6 to 7 Domestic Wells
Blue Bubbles are GSP Monitoring Wells
Larger no. of wells include monitoring, remediation, cathodic, test wells, etc.
Notes: Finally, KDWD staff spent months in the service area mapping out all equipped active wells. ID4 monitors all pumping in the ID4 area. Those are presented in the KRGSA GSP and are much more accurate than the old, inactive, and typically mis-located wells in the DWR Well completion Report files.

## Slide 38: Public Comments and Responses California Department of Fish and Wildlife
No wells occur on certain CDFW lands in the Plan Area
  Response: Other nearby wells inform local groundwater conditions
Identify habitats and species that may depend on groundwater and identify monitoring to track environmental beneficial uses over time.
  Response: NCCAG maps (TNC/DWR) and species included in GSP Section 3.3.6
Analysis merits further investigation and recommends installation of shallow monitoring wells. Also recommends additional analysis.
  Response: Shallow GSP monitoring well at Calloway Pool; additional future analysis to be considered if conditions change
No consideration of environmental uses of groundwater in management criteria.
  Response: No interconnected surface water indicated; no environmental uses of groundwater identified; sustainability goal to protect any future identified environmental beneficial uses of groundwater
DRAFT
Notes: Response: Agree, but numerous wells in the northern Plan Area provide information on groundwater conditions in the area.
Response: The analysis of interconnected surface water and GDE identification is included in the GSP (Section 3.3.6). No interconnected surface water or GDEs were identified. Shallow GSP monitoring at the area with the most healthy ecosystem on the river will continue. All Projects and Management Actions protect any missed interconnected surface water or GDEs in the Plan Area.
Response: Possible future consideration if indications of interconnected surface water in the future. Monitoring perched water is not recommended.
Response: No current environmental uses of groundwater identified so not required.
1. Not related. Over-draft mitigated through our detailed water budget.
2. Yes it is (Figure 3-34) – maybe include

## Slide 39: Additional Public Comments California Department of Fish and Wildlife
No consideration of environmental uses of groundwater in management criteria.
  Response: No interconnected surface water indicated; no environmental uses of groundwater identified; sustainability goal to protect any future identified environmental beneficial uses of groundwater
Critically over-drafted basin should not allow MTs to lower water levels.
Response: GSP brings KRGSA water budget into balance
Groundwater elevations as a proxy for water quality is not supported by correlations between concentrations and elevation.
Response: Yes it is; see Figure 3-14 Section 3.3.4.6
Anticipates involvement in CEQA for GSP projects (no response required)
DRAFT
Notes: Response: Agree, but numerous wells in the northern Plan Area provide information on groundwater conditions in the area.
Response: The analysis of interconnected surface water and GDE identification is included in the GSP (Section 3.3.6). No interconnected surface water or GDEs were identified. Shallow GSP monitoring at the area with the most healthy ecosystem on the river will continue. All Projects and Management Actions protect any missed interconnected surface water or GDEs in the Plan Area.
Response: Possible future consideration if indications of interconnected surface water in the future. Monitoring perched water is not recommended.
Response: No current environmental uses of groundwater identified so not required.
1. Not related. Over-draft mitigated through our detailed water budget.
2. Yes it is (Figure 3-34) – maybe include

## Slide 40: Next Steps
DRAFT
Board Adoption of Final GSP 12-05-2019
Additional minor revisions/cleanup of Draft GSP, as directed by the Board including clarifications in response to public comments, as needed
Final document and data preparation
Submit to DWR by January 31, 2020
Notes: Board approved Draft 8-21-2019; Published on website 8-29-2019

## Slide 41: Questions?